## Slide 1
Analyzing Architecture
Unit IV
Theory of Architecture II

## Slide 2: PRINCIPLES OF BUILDING PLANNING
Then architect prepares design of a building with the help of the following principles of planning.
  Aspect
  Prospect
  Privacy
  Roominess
  Grouping
  Circulation
  Furniture requirement
  Flexibility
  Sanitation
  Elegance
  Economy

## Slide 3: 1. ASPECT
SUN RAYS ADMITTED INTO KITCHEN
ASPECT – EAST SIDE
EAST SIDE
KITCHEN
Disposition of doors and windows in the external walls – occupants can enjoy the gifts of the nature viz; sun-shine, breeze, view of landscape etc.

## Slide 4: ASPECTS FOR DIFFERENT ROOMS
BED ROOMS
WEST
KITCHEN
EAST
STUDY ROOM
STORE
STAIR CASE
NORTH
LIVING,
VERANDAH
SOUTH

## Slide 5: 2. PROSPECT
OUTSIDE GREENEARY CANNOT BE SEEN FROM INSIDE, HENCE NO PROSPECT
FLOWER BED
WINDOW AT HIGHER LEVEL
OUTSIDE VIEW SEEN FROM INSIDE OF THE ROOM

## Slide 6: PROSPECT CONTD…
OUTSIDE GOOD SCENES, GREENARY CAN BE SEEN BY SITTING INSIDE THE ROOM, HENCE GOOD PROSPECT
WINDOW TAKEN TO LOWER LEVEL
FLOWER BED

## Slide 7: PROSPECT CONTD…
INSIDE OBSERVER
INSIDER OBSERVER
LARGE VIEW DESIRED
LESS VIEW DESIRED
CONCEALING UNDESIRABLE VIEW
INSIDE OBSERVER

## Slide 8: 3. PRIVACY
Types of privacy:
(1) Privacy of all parts of building with reference to surrounding buildings, roads etc.
  This type of privacy can be achieved by--
  Growing plants, trees etc
  Providing high windows with respect to roads, grounds etc.
(2) privacy of one room from another room:
This type of privacy can be achieved by—
  Carefully positioning of doors & windows
Exposure of the interior space / room to the visitors vision

## Slide 9: Privacy depends on placement of doors /window openings
OBSERVER
NO PRIVACY
MODERATE
PRIVACY
OBSERVER
MAX PRIVACY
OBSERVER

## Slide 10: PRIVACY CONTD…
Internal privacy can be achieved by
  Providing curtains
  Providing screens
Avoiding windows in interior walls of the room

## Slide 11: 4. ROOMINESS
Getting maximum benefit from minimum dimensions or space of room
Rectangular shaped room gives feeling of more space than square shaped room for the same area
LESS AREA AVAILABLE
MORE AREA AVAILABLE

## Slide 12: 5. GROUPING
Arrangement of various rooms in relation with their functions
KIT
LIVING
DIN
BED
STAIR
S.B.
KIT
LIVING
BED
DIN
STAIR
S.B.
GOOD GROUPING
IMPROPER GROUPING

## Slide 13: 6. CIRCULATION
Horizontal circulation – passages, corridors, verandahs etc.
Vertical circulation – stairs, lifts, escalators etc.
BAD CIRCULATION
GOOD CIRCULATION
DOOR
DOOR
DOOR
HORIZONTAL CIRCULATION

## Slide 14: 6. CIRCULATION CONTD…
VERTICAL CIRCULATION
STUDY
KIT
BED
VER
LIV
STUDY
KIT
BED
VER
LIV
BAD CIRCULATION WITH OUTSIDE STAIR
GOOD CIRCULATION WITH STAIR INSIDE
N

## Slide 15: 7. FURNITURE REQUIREMENT
Function of the Room decides the Furniture requirement of that room
  Liv hall – sofa set, teapoy, tv case, showcase, diwan etc.
  Bed – single, double beds, dressing table, almirah etc.
  Dining – dinning table, chairs, cupboards etc.
Knowing type of furniture the dimensions of the room can be arrived at.

## Slide 16: 8. FLEXIBILITY
To facilitate accommodation of changes in the plan of the building in future if necessary
ROOM 1
ROOM 2
BIG HALL

## Slide 17: 9. SANITATION
LIGHTING
  NATURAL LIGHTING
  ARTIFICIAL LIGHTING
VENTILATION
  NATURAL VENTILATION
  ARTIFICIAL VENTILATION
CLEANLINESS
SANITARY PROVISIONS
  BATHS-ROOMS
  WATER CLOSETS
  LATRINES

## Slide 18: 10. ELEGENCE
ELEGANCE MEANS THE AESHTETIC VIEW OF THE BUILDING OR THE BEAUTY OF THE BUILDING
ELEGANCE OF THE BUILDING CAN BE ACHIEVED BY
  INCREASING THE PLINTH HEIGHT OF BUILDINGS
  TREATMENT OF EXTERIOR OF BUILDING – SLOPING ROOF, PROJECTIONS ETC.

## Slide 19: ELEGENCE : CLASSROOM BUILDING

## Slide 20: 11. ECONOMY
MINIMUM DIMENSIONS OF THE ROOM, DOORS, WINDOWS,
SIMPLE DESIGN OF WINDOWS,
PROVIDING MINIMUM HEIGHT OF BUILDING
AVOIDING PORCHES, LOBBIES ETC

## Slide 21
Thank You